# Cheatsheet URL-commands BSB-LAN
URL-command	Effect
/<x>	Query value/setting of parameter <x>
/<x>,<y>,<z>	Query values/settings of parameters <x>, <y> and <z>
/<x>-<y>	Query values/settings of parameters <x> to <y>
/A	Query 24h-average values
/A=<x>,<y>	Change 24h-average value calculation of parameters <x>, <y>
/B	Query accumulated burner-runtimes (in seconds) & -cycles (incl. DHW)
/B0	Reset counter of burner-runtime and -cycles
/C	Display configuration of BSB-LAN
/D	Display logfile from the microSD-card
/DG	Graphical display of the logfile from microSD-card
/D0	Reset logfile & create new header
/E<x>	Display ENUM-values of parameter <x>
/G<x>	GPIO: Query pin <x>
/G<x>,<y>	GPIO: Set pin <x> to high (<y> = 1) or low (<y> = 0)
/G<x>,I	GPIO: Query pin <x> while setting to INPUT
/H	Query optional DHT22-sensors
/I<x>=<y>	Send INF-message to parameter <x> with value <y>
/JK=<x>	JSON: Query all parameters of category <x>
/JK=ALL	JSON: List all categories with corresponding parameter numbers
/JQ=<x>,<y>,<z>	JSON: Query parameters <x>, <y> and <z>
/JQ /JS	→ with JSON-structure (see manual) via HTTP-POST request: / Query and set parameters
/K	List all categories
/K<x>	Query all parameters and values of category <x>
/L=0,0	Deactivate logging to microSD-card (temporarily)
/L=<x>,<y1>,<y2>,<y3>	Set logging interval to <x> seconds with (optional) logging parameter <y1>,<y2>,<y3>
/LB=<x>	Configure logging of bus-telegrams: only broadcasts (<x>=1) or all (<x>=0)
/LU=<x>	Configure logging of bus-telegrams: only unknown (<x>=1) or all (<x>=0)
/M<x>	Activate (<x> = 1) or deactivate (<x> = 0) bus monitor mode
/N	Reset & reboot arduino (takes approx. 15 seconds)
/NE	Reset & reboot arduino (takes approx. 15 seconds) and erase EEPROM
/P<x>	Set busprotocol/-type (temp.): <x> = 0 → BSB | 1 → LPB | 2 → PPS
/P<x>,<s>,<d>	Set busprotocol/-type <x>, own address <s>, target-address <d> (temp.)
/Q	Check for unreleased controller-specific parameter
/R<x>	Query reset-value of parameter <x>
/S<x>=<y>	Set value <y> for parameter <x>
/T	Query optional DS18B20-sensors
/V<x>	Activate (<x> = 1) or deactivate (<x> = 0) verbose output mode
/X	Query optional MAX!-thermostats

# (… title in your language ...)
(… title in your language ...)	(… title in your language ...)
/<x>	(...)
/<x>,<y>,<z>	(...)
/<x>-<y>	(...)
/A	(...)
/A=<x>,<y>	(...)
/B	(...)
/B0	(...)
/C	(...)
/D	(...)
/DG	(...)
/D0	(...)
/E<x>	(...)
/G<x>	GPIO: (...)
/G<x>,<y>	GPIO: (...)
/G<x>,I	GPIO: (...)
/H	(…) DHT22
/I<x>=<y>	(...)
/JK=<x>	JSON: (...)
/JK=ALL	JSON: (...)
/JQ=<x>,<y>,<z>	JSON: (...)
/JQ /JS	(...)
/K	(...)
/K<x>	(...)
/L=0,0	(...)
/L=<x>,<y>	(...)
/LB=<x>	(...)
/LU=<x>	(...)
/M<x>	(...)
/N	(...)
/NE	(...)
/P<x>	(...) <x> = 0 → BSB | 1 → LPB | 2 → PPS
/P<x>,<s>,<d>	(...)
/Q	(...)
/R<x>	(...)
/S<x>=<y>	(...)
/T	(…) DS18B20
/V<x>	(…)
/X	(…) MAX!